🤖 MikroTik RouterOS 7.x
Alerts & Remote Control via Telegram
Surfshark Wireguard VPN + Device Monitor

Version 1.0 | RouterOS 7.21.1+

1. Overview
This system implements a set of scripts for MikroTik RouterOS 7.x that allow continuous router monitoring and remote control through a Telegram bot.

Main features
- Automatic alerts for Surfshark Wireguard VPN outages and recoveries
- Real-time notifications when devices connect or disconnect from WiFi (2.4GHz and 5GHz)
- Notifications when devices connect or disconnect via Ethernet
- Remote router control via Telegram commands: system status, reboot, WiFi on/off and VPN switching
- State persistence using files stored in the router filesystem

2. System Architecture
The system consists of 18 scripts organized into four categories. Monitoring scripts run autonomously via schedulers, while command scripts are launched on demand from tgCommands.

System scripts
Script	Interval	Function
config	At startup	Global configuration variables
tgSend	On demand	Sends messages to the Telegram bot
monitorVPN	30 seconds	Detects Wireguard VPN outages and recoveries
monitorDevices	15 seconds	Detects WiFi and Ethernet device connections/disconnections
tgCommands	5 seconds	Receives and processes Telegram commands (polling)
startupMsg	At startup	Sends system startup message
install	Manual	Creates all schedulers automatically

Command scripts
Script	Function
help	Shows the list of all available commands
status	Shows full system status
log	Shows the last 20 system log entries
reboot	Reboots the router with Telegram confirmation
wifi24on / wifi24off	Enables or disables the 2.4GHz WiFi interface
wifi5on / wifi5off	Enables or disables the 5GHz WiFi interface
vpn_bcn	Activates Surfshark VPN peer Barcelona (example if you have a vpn configured)
clients_connected	Shows all connected devices with MAC, IP, hostname and WiFi signal

3. Prerequisites
- MikroTik router with RouterOS version 7.x (tested on 7.21.1)
- Surfshark Wireguard VPN already configured on the router with at least one active peer
- Internet access from the router (for Telegram API communication)
- A Telegram bot created with @BotFather (see section 4.1)
- Your Telegram Chat ID (see section 4.1)
- WiFi interfaces using the /interface/wifi driver (RouterOS 7.x native, not CAPsMAN)

⚠️ Note on WiFi interfaces: The WiFi enable/disable commands use /interface/wifi which corresponds to the native RouterOS 7.x driver. If you use CAPsMAN (cap or cap-bridge interfaces) you will need to adapt those commands.

4. Step-by-Step Installation Guide
4.1. Create the Telegram Bot
1. Open Telegram and search for @BotFather
2. Send the /newbot command and follow the instructions
3. BotFather will provide a TOKEN (format: 123456789:ABCdefGHI...)
4. To get your Chat ID: send a message to your bot and visit in the browser:

https://api.telegram.org/botYOUR_TOKEN/getUpdates
Look for the "id" field inside "chat" in the JSON response.

4.2. Configure Scripts in RouterOS
In the MikroTik web interface (Winbox or WebFig), go to System → Scripts and create the following scripts. For each one, click the + button (add), enter the exact name and paste the corresponding code.

⚠️ Important: First of all, edit the config script with your Telegram token, Chat ID and the exact names of your network interfaces.

Script names to create (in this order):
- config
- tgSend
- monitorVPN
- monitorDevices
- tgCommands
- startupMsg
- install
- help
- status
- log
- reboot
- wifi24on
- wifi24off
- wifi5on
- wifi5off
- vpn_bcn
- clients_connected

4.3. Install the Schedulers
Once all scripts are created, open the RouterOS Terminal (New Terminal in Winbox) and run:

/system/script/run install

This will automatically create all necessary schedulers and send a confirmation message to Telegram.

4.4. Verify the Installation
After running the installer you should receive a confirmation message in Telegram indicating the system is active. You can verify the schedulers at System → Scheduler and check that the 4 schedulers appear.

To test the system, send the /help command to your bot and you should receive the list of available commands.

ℹ️ The tg_offset.txt file is created automatically the first time tgCommands receives a message. The deviceList.txt file is created the first time monitorDevices detects a connected device.

5. Telegram Commands
Command	Description
/help	Shows the list of all available commands
/status	Shows full status: CPU, RAM, uptime, VPN, WiFi and connected clients
/log	Shows the last 20 MikroTik system log entries
/reboot	Reboots the router (waits 3 seconds before executing)
/wifi24on	Enables the configured 2.4GHz WiFi interface
/wifi24off	Disables the configured 2.4GHz WiFi interface
/wifi5on	Enables the configured 5GHz WiFi interface
/wifi5off	Disables the configured 5GHz WiFi interface
/vpn_bcn	Activates Surfshark VPN peer Barcelona
/clients_connected	Shows all connected devices: network, hostname, IP, MAC and WiFi signal

6. Automatic Alerts
Emoji	Event	Information included
🔴	Surfshark VPN down	Interface name, date and time of event
🟢	Surfshark VPN recovered	Interface name, date and time of recovery
📶	WiFi device connected	Network (2.4G/5G), hostname, IP, MAC, signal, time
📴	WiFi device disconnected	Network (2.4G/5G), hostname, IP, MAC, time
🔌	Ethernet device connected	Ethernet interface, hostname, IP, MAC, time
🔌	Ethernet device disconnected	Ethernet interface, hostname, IP, MAC, time
🟢	Router started/rebooted	RouterOS version, hardware, boot time

7. Surfshark VPN Management
The system allows switching between different Surfshark Wireguard VPN peers configured on the router. Each VPN has its own dedicated script following the same paradigm as the rest of the commands.

How it works
- The script disables ALL active Wireguard peers
- Enables the desired peer by exact name
- Verifies the peer is active after the switch
- Reports the result via Telegram with ✅, ⚠️ or ❌

Adding a new VPN
To add a new VPN server, copy any vpn_* script, rename it (e.g. vpn_mad) and change only the targetPeer variable with the exact name of the Wireguard peer:

# SCRIPT: vpn_mad
# Description: Activates Surfshark VPN peer Madrid
:local targetPeer "wireguard-peer-MAD"

The script name determines the Telegram command: the vpn_mad script is triggered by the /vpn_mad command.

8. State Persistence
The system uses two files to maintain state between executions:

File	Contents
tg_offset.txt	Last processed Telegram update_id. Prevents processing the same message twice.
deviceList.txt	List of currently connected devices in CSV format. Allows detecting connections and disconnections.

ℹ️ These files are created automatically. If deleted, tg_offset.txt will be recreated with the next received message. If deviceList.txt is deleted, all currently connected devices will be notified as new on the next monitorDevices execution.

9. Troubleshooting
Bot does not respond to commands
- Verify that the tgCommands scheduler is active in System → Scheduler
- Check that the TOKEN and CHAT_ID in the config script are correct
- Review the system log (/log/print in terminal) for connection errors
- Check that tg_offset.txt is not blocking messages with a too-high offset

No VPN alerts arriving
- Verify the interface name in vpnInterface matches exactly the name in /interface/wireguard/
- Check the monitorVPN scheduler is active
- Verify the global variable vpnWasUp is initialized (run config manually)

WiFi or Ethernet devices not detected
- Verify the interface names in wifi24Interface and wifi5Interface are correct
- Check the interface uses the /interface/wifi driver (RouterOS 7.x)
- WiFi clients must appear in /interface/wifi/registration/find
- Ethernet devices are detected via ARP table (/ip/arp/find complete=yes)

Fetch/connection errors
- Make sure the router has Internet access
- If the VPN is down and traffic goes through it, alerts will also fail
- Configure a fallback route so that api.telegram.org traffic does not use the VPN

WiFi commands not working
- Verify you are using RouterOS 7.x with the /interface/wifi driver
- If using CAPsMAN, adapt the commands to /interface/cap

10. Customization
Adjust execution intervals
Edit the values in the config script:

:global vpnCheckInterval 30 # VPN interval in seconds
:global deviceCheckInterval 15 # Device interval in seconds
:global telegramPollInterval 5 # Telegram polling interval in seconds

Time-based alerts
To receive alerts only during certain hours, add at the beginning of the monitoring scripts:

:local hour [:tonum [:pick [/system/clock/get time] 0 2]]
:if ($hour < 8 || $hour > 22) do={ :error "Outside schedule" }

This would send alerts only between 08:00 and 22:00.

Add new VPN servers
Copy any vpn_* script, rename it and change the targetPeer variable with the exact name of the Wireguard peer. The new command will be available automatically via Telegram with /script_name.

Add custom commands
Create a new script in System → Scripts with the command name (without the /). For example, for the /temperature command create a script named temperature. tgCommands will detect it and launch it automatically.

End of document